## Slide 1: The Sound of Digital Transformation
TechnologEEE Arduino Program
NJ
Equip|Educate|Encourage
TechnologEEE

## Slide 2: What is Digital Transformation?
Digital Transformation is the integration of digital technologies into all aspects of business and human society
NJ
Equip|Educate|Encourage
TechnologEEE
Notes: AT&T – Analog switches and NFV
Digital Transformation also affects how businesses operate

## Slide 3: Exercise Introduction
Build a piano using the Arduino and button switches
Digitize the button switches in the program
NJ
Equip|Educate|Encourage
TechnologEEE

## Slide 4: Materials
1 Arduino USB cable
Wires
5 100 Ohm resistor
(brown-black-black-black-brown)
1 Arduino Uno
1 breadboard
5 blue LEDs
5 Button Switches
1 active buzzer
NJ
Equip|Educate|Encourage
TechnologEEE

## Slide 5: Arduino Intro
Arduino is an open-source electronics platform based on easy-to-use hardware and software.
It's intended for anyone making interactive projects.
NJ
Equip|Educate|Encourage
TechnologEEE

## Slide 6: LED intro – Light Emitting Diode (LED)
NJ
Equip|Educate|Encourage
TechnologEEE
Notes: Explain LEDs – Light emitting diode, more commonly known as an LED, that is a two lead semiconductor source. It is a p-n junction diode, which emits light when activated. More simply, if you put a power source to the right end, it will light up.
Explain/Identify cathode and anode – The cathode is the negative end and the anode is the positive end. You can tell which is which by identifying which is the shorter end and which is the longer end. The anode is the longer end and the positive side. The cathode is the shorter end and the negative side. This will be important for making the traffic light, so remember this. Maybe, make a pneumonic.
Tell kids to take LEDs and make a wider V (suggestion)

## Slide 7: Button Switch Intro
Controls whether a circuit is open or closed, whether electricity flows through the circuit or not
Pressing the button means closing the switch, connecting 1-2 to 3-4
NJ
Equip|Educate|Encourage
TechnologEEE

## Slide 8: Active Buzzer Intro
When a DC voltage is applied, an oscillator is activated
An oscillator is a piece of material that vibrates when current flows through it
These vibrations make noise, just like your vocal chords
NJ
Equip|Educate|Encourage
TechnologEEE

## Slide 9: Adding the Switches
Place 5 buttons with their legs plugged into the following holes:
  Button 1: e5, e7, f5, f7
  Button 2: e10, e12, f10, f12
  Button 3: e15, e17, f15, f17
  Button 4: e20, e22, f20, f22
  Button 5: e25, e27, f25, f27
NJ
Equip|Educate|Encourage
TechnologEEE

## Slide 10: Creating Circuits
Connect resistors to the switch:
  Place a resistor from (+)7 to d7
  Place a resistor from (+)12 to d12
  Place a resistor from (+)17 to d17
  Place a resistor from (+)22 to d22
  Place a resistor from (+)27 to d27
Connect LEDs to the switch:
  LED1: short leg in (-)5, long leg in a5
  LED2: short leg in (-)10, long leg in a10
  LED3: short leg in (-)15, long leg in a15
  LED4: short leg in (-)21, long leg in a20
  LED4: short leg in (-)25, long leg in a25
NJ
Equip|Educate|Encourage
TechnologEEE

## Slide 11: Adding the Buzzer
Buzzer: place the short end in e50, long end in f50
Connect Power and Ground:
  Connect 5V on the Arduino to (+)55
  Connect GND on the Arduino to (-)60
Connect digital 9 on the Arduino to i50
NJ
Equip|Educate|Encourage
TechnologEEE

## Slide 12: Adding Digital Inputs
Connect wires from the switches to the Arduino
  Connect a wire from j5 to Arduino digital 2
  Connect a wire from j10 to Arduino digital 3
  Connect a wire from j15 to Arduino digital 4
  Connect a wire from j20 to Arduino digital 5
  Connect a wire from j25 to Arduino digital 6
NJ
Equip|Educate|Encourage
TechnologEEE

## Slide 13: Uploading the Code
Plug the Arduino into the laptop with the USB cable
Open “piano.ino”
Map the COM port to the Arduino and upload the code
Can modify the code to change the frequencies
NJ
Equip|Educate|Encourage
TechnologEEE

## Slide 14: Digitizing the Piano Setup
Open “piezo.ino”
Upload the code to the Arduino
NJ
Equip|Educate|Encourage
TechnologEEE

## Slide 15: Sample Discussion Questions
Can you think of any ways you can further digitize this piano setup?
What are the benefits of having the digital setup vs the analog? What are the challenges?
Can you think how this transition to digital technologies affect the way businesses operate?
NJ
Equip|Educate|Encourage
TechnologEEE